## Slide 1: Verification
Spring 2022
Tufts University
Instructors: Joel Grodstein, Scott Taylor
Generating stimulus

## Slide 2: Outline of this lecture
Random & directed – the basics
FPU case study
CPU case study
Fancy stuff: machine learning
Error injection

## Slide 3: Generating test content
Word association game
  More the better 
So – how do you generate stimulus, and lots of it?
Aside: we know now there’s more to verification than generating stimulus, right?
  Review – but what exactly?
  Well: monitors, checkers, coverage measures, …
good verification
write lots of tests

## Slide 4: Directed vs. random
Directed
  you decide exactly what test to write
  you (a human) write it
Random
  not quite fully-random input!
  you write a “template”
  template + randomization = lots of tests
Pros & cons? Quality vs. quantity?
  Sometimes, to some extent, yes 
  Cost is not the only issue with directed testing

## Slide 5: Writing a test is hard!
Humans are lousy at thinking of corner cases
  so we never know what test to write
Control from the pins is hard
  yet again (we’ve seen this issue multiple times)
  we may know what to test deep in the machine
  it’s hard to make that happen from the inputs
stuff
other
stuff
my stuff
inputs
outputs
(good)
Notes: We try to think of the corner cases that the designer missed – but if they were easy to think of, the designer would have thought of them too!

## Slide 6: Does randomness work?
Does it seem weird that random tests can do better than a human at making something happen deep inside?
  maybe it’s not as efficient
  there’s a lot to be said for letting a machine crank stuff out while you relax on the beach 
stuff
other
stuff
my stuff
inputs
outputs

## Slide 7: Mesh in a system
Start with the mesh
Declutter the drawing
  but really the routing links are still there!
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 8
Add the mesh drivers and receivers
  Pr=processor
  Ca=cache
  MC=memory controller
  Gr=graphics
  DD=disk drive controller
  Pr & Ca might be combined
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Ca
Ca
Ca
Ca
Pr
Pr
Pr
Pr
MC
MC
IO
IO
Gr
Gr
DD
DD

## Slide 9: Bug
When Pr1, Pr2, MC1 all interact with Ca1:
  Pr1 wr-requests L
  Ca1 evicts L, Pr2 rd-req L
  MC1 fills any line
This exposes Ca1 bug 
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Ca
Ca
Ca
Ca
Pr
Pr
Pr
Pr
MC
MC
IO
IO
Gr
Gr
DD
DD

## Slide 10: Way too many cross products!
Cannot test all interactions between 4 entities!
  You can test a random subset
Again: no guarantees, but it’s about the best you can do
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Ca
Ca
Ca
Ca
Pr
Pr
Pr
Pr
MC
MC
IO
IO
Gr
Gr
DD
DD

## Slide 11: Outline of this lecture
Random & directed – the basics
FPU case study
CPU case study
Fancy stuff: machine learning
Error injection

## Slide 12: What’s in a float?
IEEE 754 has various classes of numbers
  zero, infinity, NaN
  denormals
  everything else!
Rules of the new math
  2x2 =
  1 / 0 =
  ∞ + ∞ =
  -1 / 0 =
  ∞ - ∞ =
  0 / 0 = ∞/∞ =
4
∞
∞
-∞
NaN
NaN
That’s everything except
  -0 vs. +0
  denormals
Notes: Negative and positive zero is because we use sign+magnitude rather than 2s complement
Denormals are a special case for very small numbers (more later).

## Slide 13: Number line
Here’s the number line (sort of)
-0 +0
denormals
+∞ NaN
NaN -∞
everything else
everything else
Notes: Note that there is no “negative” vs. “positive” NaN; the spec says that the sign bit is ignored for NaN

## Slide 14: What should we test?
The special cases are a small fraction of total area
  which parts are most important?
  what should our strategy be?
Where do you think the bugs are?
  the “weird” stuff; denorms, infinity, etc?
  Or not – maybe the designer spent the most time on that!
-D -0 +0 +D
+∞ NaN
NaN -∞
Notes: Mention in passing that 2^32 choices for each operand is too many to test exhaustively (there will be a quiz question later on the details).

## Slide 15: More corner cases
FPUs have well-known critical paths
  designers do headstands to make their FPU run fast
  do those headstands cause their own corner cases?
How might you (the verif. engineer) even know what headstands were done?
  ask the architect

## Slide 16: Trust or verify?
Perhaps the architect says:
  I love that denormal stuff; all those special cases were really interesting & I know I got it right
  I hate infinity, honestly I just wrote some junk to make my coding deadlines & it’s probably buggy
  I’m pretty sure I got most of the rest right
So what content strategy do you use?
  Write lots of manual tests for ∞, none for denorms, a few for the rest, and you’re done?
Question: how much do you believe your favorite architect?

## Slide 17: Trust or verify?
How many tests did you believe you:
  would ace and didn’t?
  would fail and didn’t?
By and large, your guesses about preparedness were probably mostly correct
  but would you bet project success on it?

## Slide 18: Trust or verify?
Wisdom though the ages
  “The known unknowns are are things that we know we don’t know. But there are also unknown unknowns. There are things we don’t know we don’t know.” Donald Rumsfeld, 2002
  “It’s the issues you didn’t predict that get you. You never know just what you don’t know until it’s too late.” Nobody in particular
But how do you translate this wisdom into resource allocation for FPU test content?

## Slide 19: Purely random?
-D -0 +0 +D
+∞ NaN
NaN -∞
Pick purely random operands, operations?
  Would that work well?
Rarely hits corner cases
  232 choices for each operand
  odds of picking 0, ∞, NaN are very low
  odds of fleshing out corner cases of these values with a purely random approach are vanishingly low 
Any better ideas?

## Slide 20: Knobs & weights
Pick operand
  denorm_frac odds of being a denorm
  special_frac odds of being NaN, ∞, 0
  else a “normal” float
  then pick exact operand randomly
Pick operation
  add_frac, divide_frac, etc.
These controls are called knobs or weights
  give you high-level control of your randomness
  tailor them to your needs
First pick class
Then pick value

## Slide 21: In-class exercise
Perhaps the architect says:
  I love that denormal stuff; all those special cases were really interesting & I know I got it right
  I hate infinity, honestly I just wrote some junk to make my coding deadlines & it’s probably buggy
  I’m pretty sure I got most of the rest right
Pick operand
  denorm_frac odds of being a denorm
  special_frac odds of being NaN, ∞, 0
  else a “normal” float
  then pick exact operand randomly
Pick operation:
  add_frac, divide_frac, etc.
How will you set the knobs?
Notes: Let them figure this out now. Probably roughly follow what the architect said, but with lots of deference to your own feelings, and past experience with previous FPUs.

## Slide 22: Outline of this lecture
Random & directed – the basics
FPU case study
CPU case study
Fancy stuff: machine learning
Error injection

## Slide 23: CPU testing
Designing an RCG for our simple FPU was easy 
  But a CPU is bigger & more complex 
  Can we do something similar?
What was the hardest part of EE126 design?
  Pipeline stalls?
  Forwarding?
  Getting branches right?
Can we design a CPU RCG that generates tests roughly targeted at the buggy areas?
a.k.a. “most likely to have bugs!”
Notes: and by “hardest”, I mean “most likely to have bugs!” Especially in the pipelined version

## Slide 24: RCG
Can we build a Random-Code Generator (RCG)?
Start with a completely random sequence of instructions – any issues?
  arithmetic:
  branches:
  memory:
So completely random testing isn’t great. Next idea?
what about divide by zero?
what about infinite loops? And how do we know if the test passed?
load before store → unpredictable results
Notes: Little historical note – RCG is literally random code – but the term RCG is now used for most any random test driver.
The “how do we know if the test passed” issue for branches is that merely taking a branch doesn’t change any architectural register, so we may not be able to figure out after the fact which branch was taken.

## Slide 25: Exercise: can you fix the issues?
Start with a completely random sequence of instructions – any issues?
  arithmetic:
  branches:
  memory:
what about divide by zero?
what about infinite loops? And how do we know if the test passed?
load before store → unpredictable results
Can you slightly modify the random code sequences to avoid these problems?

## Slide 26: Exercise: can you fix the issues?
Arithmetic:
  can do random ops, and then…
  throw away the divide-by-zero and similar tests
  They should be a small fraction of all tests
Branches
  analyze the random programs, remove infinite loops?
  and put different loads after each branch path?
Memory
  Do loads in store+load pairs
  Move them randomly but always put the store first
Are the fixes starting to sound a bit algorithmic rather than random?
  Yes! We call that a template
what about divide by zero?
what about infinite loops?
How do we know if the test passed?
load before store → unpredictable results
Notes: Note that these suggestions are going away from our totally-random approach. In particular, the memory one seems more algorithmic than random, and the “loads after branches” seems a bit algorithmic also.

## Slide 27: Templates
We really want our same FPU strategy
  target buggy areas
  in proportion to expected bugginess
But a single instruction won’t do a useful test
  need a coherent group of instructions working together
A template
  gives your test a structure, order, global logical sense
Then knobs
  control the details of what to randomize
  and within what constraints

## Slide 28: Knobs & weights
Pick operand
  denorm_frac odds of being a denorm
  special_frac odds of being NaN, ∞, 0
  else a “normal” float
  then pick exact operand randomly
Pick operation
  add_frac, divide_frac, etc.
These controls are called knobs or weights
First pick class
Then pick value
Would you still call these knobs, or are they really templates?
What might a template be for the FPU?
Notes: A template for the FPU might control a bigger sequence; maybe you always wrap three FPU ops between a load & store for some reason, and also run a power virus.

## Slide 29: St/ld template
We had reordered st/ld pairs; here’s another template
Pick N1 random addresses
Store random values → all of them
Repeat N2 times:
  pick one of the known addresses
  Ld → random register
  Store a random known register → random address
How might we check results?
now there are more known addresses
now there are more known registers
Notes: Remember that we are randomizing stuff in our stimulus generator (which is part of the TB).
The point is that the TB knows what we wrote, so it can finish up by checking that memory and registers are all correct.
This isn’t perfect – we may write a single location multiple times, & we only check the final value. More on that shortly!

## Slide 30: 2-way set-associative cache
data
<<
index
=
hit?
=
sets
[4:0]
[13:5]
[31:14]
3FE
1FF
7FE
11FF
1000
1
202
0
201
402
T
T
T
way #0 way #1
set #0
set #1
T
T
T
T
T
T
T
Refresher from EE126 
How do you pick Ld/St addresses to stress cache misses without needing lots of stores, loads?
Notes: You pick addresses that are in the same set. I.e., lots of addresses with the same addr[13:5] but different addr[31:14].

## Slide 31: Knobs
Pick N1 random addresses
Store random values → all of them
Repeat N2 times:
  pick one of the known addresses
  Ld → random register
  Store a random known register → random address
What knobs might control this template (given our L1 knowledge)?
How might you enhance it?
same cache line or set
fraction to existing vs. new addr?
Notes: Same cache line or block is interesting. We can control L1 hits vs. misses via same cache line. We can control L1 evictions and L2 usage by using lots of addresses in the same set.
The “fraction to existing vs. new addr” is the same idea.
The “store with random values” is probably just to be able to better check the results, and “random” could just be “different” instead.

## Slide 32: Constraints – details
How do you pick lots of addresses with
  the same value for addr[13:5]
  different values for addr[31:14]
addr_13_5 = $urandom_range (9'h1FF);
for (int i=0; i<10; ++i) begin
  addr_31_14 = $urandom_range (18'h3FFFF);
  addr = { addr_31_14, addr_13_5, 5'h0 };
end
SystemVerilog has an extensive facility for constrained randomization
  Spear chapter 6
  https://www.systemverilog.io/randomization
Notes: Strictly speaking, this code snippet just overwrites the same variable addr. But you get the idea 

## Slide 33: Discussion
Mesh lab #2 asks you to build an RCG to drive the mesh
How could it work?
What knobs will be useful for your mesh RCG?

## Slide 34: Outline of this lecture
Random & directed – the basics
FPU case study
CPU case study
Fancy stuff: machine learning
Error injection

## Slide 35: Knobs & weights
Pick operand
  denorm_frac odds of being a denorm
  special_frac odds of being NaN, ∞, 0
  else a “normal” float
  then pick exact operand randomly
Pick operation:
  add_frac, divide_frac, etc.
These controls are called knobs or weights
  give you high-level control of your randomness
  tailor them to your needs
Exercise – how will you set the knobs?
  what the architect said + your own experience
Remember this slide?
How much do we trust anyone’s intuition?
Can we do better?
Notes: We said we would set the knobs based of a combination of where the architect thought the bugs are, plus our own intuition and past experience. But really, all of that is just guesses. What if we don’t trust anyone’s predictions, including our own?

## Slide 36: Genetic algorithms
denorm_frac | .3
special_frac | .2
add_frac | .4
mpy_frac | .2
denorm_frac | .5
special_frac | .3
add_frac | .3
mpy_frac | .6
denorm_frac | 
special_frac | 
add_frac | 
mpy_frac | 
mating
.3
.2
.3
.3
denorm_frac | .5
special_frac | 
add_frac | .3
mpy_frac | 
.3
.6
mutation
.4
.5
Mate and mutate knob settings
When you have no idea, try machine learning 

## Slide 37: Genetic algorithms
Start with 10 different knob combinations
  Run 100 tests with each; which finds the most bugs?
  Keep the 2 best knob combos
  Try some mutations of those 2 best
  Add some matings between those & others, etc
Automatically play with knobs, see what works
What key assumption might make this work?
  there are some patterns; the bugs you’ve found can predict the ones you haven’t
  past performance predicts future results

## Slide 38: Reasonable?
Key assumption:
  the bugs you’ve found can predict the ones you haven’t
  past performance predicts future results
But do you think the assumption is reasonable?
Notes: If the knob is load/store vs. arithmetic, and in fact the guy who designed the ld/store unit is incompetent, then yes – it’s quite reasonable.
If we’ve trying to find the right knob to work through 10 queues and hit bad cache timing, then probably not.

## Slide 39: Genetic alg + coverage
Our metric: success = most bugs found
Another metric for a GA: most coverage
  will revisit after we discuss coverage

## Slide 40: Many Rats
Once you find a bug, what do you do?
  pat yourself on the back 
  fix it
  launch a Many Rats task force
Many rats
  what does this bug say about design methodology?
  About people?
Intuition – trying to decide if past performance does predict future results
  and if so, is there a good way to explore this area of the design more thoroughly?
  “an island of directed in a sea of random”
Notes: If you’ve found one rat in your kitchen, there are probably more!
“An island of directed in a sea of random” is a quote from Jim Huggins. It means that you have a ton of random content that finds problematic areas, and then a set of directed tests that explore those areas more fully.

## Slide 41: Many-rats example
An IP vendor updated the spec of their IP without really warning Nvidia, causing a bug
What’s a reasonable many-rats plan?
  call the vendor and ask if there are any other unannounced spec releases
  look through all the other IP vendors’ docs and see if there were any updates
Notes: #2 is what actually happened

## Slide 42: Outline of this lecture
Random & directed – the basics
FPU case study
CPU case study
Fancy stuff: machine learning
Error injection

## Slide 43: Divide by zero
We’ve tried not to do things like /0
  how good is that strategy?
  probably not very!
Actual programmers divide by 0 all the time
  CPU architecture specifies exception-handling rules
  it’s probably a corner case!
  we must test this too!
How? the usual strategies…
  first set up all the exception vectors so you know what happened
  one directed /0 test?
  RCG combining multiple exceptions in the same cycle?
Arithmetic: can do random ops, and then…
  throw away the /0 and similar tests
  They should be a small fraction of all tests
Remember this?

## Slide 44: Broken mesh links
Remember what the mesh looks like? 
Let’s talk about broken links
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 45: Broken mesh links
Why do we care about broken links?
  Hopefully this is pretty obvious!
All links will eventually fail
Big question – then what?
  Does the network fail? Get slower? How much slower?
Is resilience a big selling point for networks?
  How might you compare its importance to bandwidth, latency?
  99.999% uptime
Notes: And anytime we have an important feature – we have to verify it!

## Slide 46: Verifying resilience
What do we have to verify?
  One broken link? Two? More? Why?
Any ideas how we might verify resilience?
  Do we have a separate model with a broken link?
  Separate models for all combinations of two broken? Three?
  Better solution: the verification environment clobbers links
  Do we do this randomly or directed?
Lookahead – mesh-challenge lab is exactly this
Notes: If one broken link is rare, do we need to model two or more broken links? Depends on the cause. A snowstorm could cause lots of downed lines. Ditto for an electrical failure in a neighborhood. Perhaps less likely to have two broken links in one chip – but perhaps a wafer at an unusual process corner.

## Slide 47: Error injection
Any other “errors” to test for?
  i.e., an unusual event with a specific response
  Single-bit memory errors, noise in packet transmission, broken links, …
These are typically bug farms!
All of this needs to be tested
  often lots of special-purpose directed tests

## Slide 48: CrashMe
CrashMe
  RCG from U. Michigan, 1990s
  Literally wrote random bits and called it code!
What do you think the results were? Useful?
Notes: Actually, it was amazingly effective at crashing operating systems .
One user running CrashMe could take down the O/S or at least crash other users also.
Neither the CPU designers nor the O/S writers had ever expected to see truly random bits!
I (Joel) wonder if this is a bit of an urban legend – you would think that trying to execute a data file would be fairly commonplace.

## Slide 49: BACKUP

## Slide 50: Floating-point math unit
IEEE 754 standard:
  Start with mantissa and exponent
  25 = 2.5 x 101
  512 = 5.12 x 102
  .15 = 1.5 x 10-1
But it’s really in binary, not decimal!
  3 = 0b11 = 1.1 x 21
  11 = 0b1011 = 1.011 x 23
  .75 = 0b .11 = 1.1 x 2-1
1.0 ≤ mantissa < 10
1.0 ≤ mantissa < 2

## Slide 51: Now make it sneaky
Our numbers, again
  3 = 0b11 = 1.1 x 21
  11 = 0b1011 = 1.011 x 23
  .75 = 0b .11 = 1.1 x 2-1
The first mantissa bit is always “1”
  So don’t bother storing it!
  Called a “hidden bit”
1.0 ≤ mantissa < 10
31 30 23 22 15 7 0
sgn exp mantissa

## Slide 52: IEEE 754 summary
Number =
Range: 0x00000000 = 2-127
0x7FFFFFFF = (1+.999) ∙ 2128 ≈ 2129
But we’re not quite done yet 
  How can we represent zero?
31 30 23 22 15 7 0
sgn exp mantissa

## Slide 53: Denorms and special numbers
Number =
Exponent range
  exponent=0 → [2-127, 1.999*2-127]
  exponent=1 → [2-126, 1.999*2-126]
Reserve a few patterns for +∞, -∞, NaN
And that’s it!
  well, plus rules for rounding, working with ∞, NaN, etc.
31 30 23 22 15 7 0
sgn exp mantissa
[0, 1.999*2-127]
Notes: When you cover [0,1.999*2^(0127)] in the same 23 bits of mantissa, the spacing between the numbers gets bigger; and that’s before reserving the special patterns.
Exponent=0x00 is denorms; (-1)^sign * mantissa/2^23 * 2^-126.
Exponent=0xFF is special. Mantissa=0 is infinity; mantissa not 0 is all NaN.