## Slide 1: Verification
Spring 2022
Tufts University
Instructors: Joel Grodstein, Scott Taylor
Coverage

## Slide 2: Outline of this lecture
What is coverage and why do you care?
Code coverage and toggle coverage
Functional coverage
Using your coverage numbers and filling holes
Examples

## Slide 3: Are we done yet?
With directed tests, you know when you’re done
  20 directed tests to write
  you’ve written 15
  you’re 75% done 
Knowing how close you are to being finished is very useful. Why?
  schedule planning

## Slide 4: RCGs are harder 
RCGs are great
  create a million tests while you’re at the beach
  but how many is enough?
  how do you know when you’re done?
Dilemma
  schedule planning seems impossible
  but necessary
  your manager will hound you
Measure coverage → know what features have been tested
  you regain schedule control
  have tested 15 / 20 features → 75% done?
Our problem for this lecture
The solution
Notes: Coverage is a magic “sensor” that tells you what all of these random tests have actually tested!
We’ll talk about how it works, but that’s what it is.
15/20 is probably not 75% done in terms of effort, due to diminishing returns.

## Slide 5: Outline of this lecture
What is coverage and why do you care?
Code coverage and toggle coverage
Functional coverage
Using your coverage numbers and filling holes
Examples

## Slide 6: What is “coverage?”
Coverage is a magic measurement tool
  tells you what the 1M random tests have actually tested
Types of coverage:
  code coverage: line coverage, condition coverage
  toggle coverage
  functional coverage
Notes: See the next slide for details…

## Slide 7
line coverage
  how often was each line of code executed?
condition coverage
  was every if both taken and not?
always_ff @(posedge clk) begin
  if (wr_en) begin
    fifo_mem[wr_ptr] <= wr_data;
  wr_ptr <= wr_ptr+1;
  end
  return
  a bunch more code
end
  Question: does 100% condition coverage imply 100% line coverage?
toggle coverage
  was every signal set to both 0 and 1?
Notes: you can have 100% condition coverage, but bad line coverage; e.g., if lots of code is in an always block that never gets executed. Or you don’t cover all options in a Case statement.
toggle coverage gets tricky for multi-bit signals. QuestaSim just breaks them down and gives you each bit individually, which is not always what you want. Different tools may be different, and QuestaSim have various options, but this is pretty typical (if not perfect).

## Slide 8: Pros/cons
line coverage
condition coverage
toggle coverage
always_ff @(posedge clk) begin
  if (wr_en) begin
    fifo_mem[wr_ptr] <= wr_data;
  wr_ptr <= wr_ptr+1;
  end
end
Pros
  the simulator measures them all for you! No work
Cons
  can leave out features altogether & get 100% coverage
  toggle coverage not always useful for multi-bit controls
  <100% coverage may not be an issue (Why?)
  Covering something doesn’t mean the result is visible
Notes: Why might it be OK to have <100% line/condition/toggle coverage? Surprisingly many lines may be dead code! Or features that aren’t needed until later. Or the multi-bit issue on toggle coverage; do you really need every bit combination of a multi-bit signal?

## Slide 9: Outline of this lecture
What is coverage and why do you care?
Code coverage and toggle coverage
Functional coverage
Using your coverage numbers and filling holes
Examples

## Slide 10: Functional coverage
What does functional coverage mean?
  whatever you want it to 
You decide what is important!
  which signals, which values
  you tell the simulator (covergroups)
  it checks that they’re covered
Good news – responsibility is on your shoulders!
Bad news – responsibility is on your shoulders!
you get to define what’s important
your boss knows who to blame

## Slide 11
Brainstorm: what might be good coverage for the FIFO?
  All combinations of read & write pointers?
  Just empty & full?
  Others?
Regfile
Rd ptr
(3-bit ctr)
Wr ptr
(3-bit ctr)
Data_in
Data_out
WR
RD
Notes: Arguably all ptr combinations are irrelevant.
We’ve talked about error conditions – somebody should also check reading an empty FIFO and writing a full one

## Slide 12: Pros/cons
Can be lots of work!
  analyze your spec, verification plan
  decide what’s important and what’s not
  tell that to the simulator (build the covergroups)
  analyze the results & change course (more later)
Versus code coverage
  code coverage: do your tests exercise the RTL?
  functional coverage: do your tests exercise the spec?
And remember…
  analyzing code coverage takes forever
  designing good functional coverage takes forever
  but so does writing a bazillion directed tests
Can somebody interpret this?
Education is expensive, but so is ignorance
Notes: the relevant quote – if you think education is expensive, so is ignorance

## Slide 13: Directed tests
Coverage is good for directed tests, too
Any idea why?
  your test may not be testing what you think it is!
  it may stop testing what it used to test (see next slides)
bit test_passed;
test_passed = part1_pass | part2_pass | part3_pass;
Notes: Somebody wrote “or” rather than “and”, so the test inadvertently passes even though most of it fails.
And the other reasons will be on the next few slides.

## Slide 14: Bug
When Pr1, Pr2, MC1 all interact with Ca1:
  Pr1 wr-requests L
  Ca1 evicts L, Pr2 rd-req L
  MC1 fills any line
This exposes Ca1 bug 
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Ca
Ca
Ca
Ca
Pr
Pr
Pr
Pr
MC
MC
IO
IO
Gr
Gr
DD
DD
Remember this?

## Slide 15: Cross products
You find the bug and fix it. What if it breaks again?
  Wait until the RCG randomly hits that case again?
  No, save the bug-finding test & re-run it often
What if:
  the bug reappeared, and the mesh timing changed?
  Old test won’t work any more 
  You save the coverage point
When Pr1, Pr2, MC1 all interact with Ca1:
  Pr1 wr-requests L
  Ca1 evicts L, Pr2 rd-req L
  MC1 fills any line
what do you think that even means?
Notes: What does it mean to save the coverage point? It means that after finding the bug, now we know that uncovering the shared resource is an important cross product. So our functional coverage says that – i.e., that we must have a test where the four events collide. Now when they change the mesh timing, our coverage data immediately tells us that our old test doesn’t work any more

## Slide 16: Key point
Specify functional-coverage goals = specifying what the interesting design states are
  e.g., you better set up a pipeline resource conflict
  smarter than tweaking pipe timing in a directed test!

## Slide 17: Outline of this lecture
What is coverage and why do you care?
Code coverage and toggle coverage
Functional coverage
Using your coverage numbers and filling holes
Examples

## Slide 18: Big-picture strategy
coverage keeps rising?
Y
N
don’t worry, be happy
coverage plateau. At ≈ 100%?
You need a better RCG
Done 
Full coverage 
Still finding bugs?
Improve coverage targets
Y
N
Y
N
Exercise – fill in the “?” labels
?
?
?
?
Notes: Another interesting case: what if functional coverage numbers are low but code coverage is high? Maybe they forgot to code a feature altogether

## Slide 19: Big-picture strategy
coverage keeps rising?
Y
N
don’t worry, be happy
coverage plateau. At ≈ 100%?
You need a better RCG
Done 
Full coverage 
Still finding bugs?
Improve coverage targets
Y
N
Y
N
How do you do this?

## Slide 20: Filling coverage holes
“Improve your RCG”
  easy to say, but perhaps hard to do!
First, analyze your plateau
  which areas are not being covered?
Example – L2 cache evictions still uncovered
  so alter the RCG constraints to target that
  remember how?

## Slide 21: 2-way set-associative cache
data
<<
address
=
hit?
=
sets
[4:0]
[13:5]
[31:14]
@3FE
@1FF
@7FE
@11FF
@1000
@1
@202
@0
@201
@402
T
T
T
way #0 way #1
set #0
set #1
T
T
T
T
T
T
T
Refresher from EE126 
How do you pick Ld/St addresses to stress L1 misses?
Remember this?
Notes: You pick addresses that are in the same set. I.e., lots of addresses with the same addr[13:5] but different addr[31:14].

## Slide 22: Exercise
We find a coverage hole: L2 evictions
  Can we change our RCG knobs to stress that?
What if the L2 were mapped differently?
[4:0]
[13:5]
[31:14]
L1
[4:0]
[16:5]
[31:17]
L2
[4:0]
[31:20]
[19:5]
L2
Notes: Now we’ll pick addresses with the same addr[16:5], not just [13:5].
With the new mapping, we would need the same addr[30:20,13:5].
Talking point: many modern CPUs actually do an XOR hash of addresses to pick the set – targeting can get complicated!

## Slide 23: Outline of this lecture
What is coverage and why do you care?
Code coverage and toggle coverage
Functional coverage
Using your coverage numbers and filling holes
Examples

## Slide 24: FIFO coverage
Remember our FIFO? What should we check?
  Start with read and write pointers
  Do they each cycle through all values?
Regfile
Rd ptr=
Wr ptr=
Data_in
Data_out
WR
RD
Empty=
Full=

## Slide 25: Coverage code
covergroup fifo_cg
  @posedge(clk) if (!reset);
  coverpoint rd_ptr, wr_ptr;
endgroup
Define a coverage group, give it a type name
Get coverage on the read & write pointers
Only collect coverage at r.e. of clock
And not when we’re in reset

## Slide 26: What coverage exactly?
Rd_ptr and wr_ptr are 3 bits each
  So build two 8-bin histograms
Regfile
Rd ptr=
Wr ptr=
Data_in
WR
RD

## Slide 27: Code to instantiate
Any idea why SV bothered to have this class-like syntax?
  So that we can instantiate many of them
Why would we ever want to make more than one fifo_cov?
  Just wait a few slides…
module tb_top
  fifo #(N_ADDR_BITS, FIFO_WIDTH) F (.*);
  covergroup fifo_cov @(posedge clk) if (!reset);
  coverpoint F.rd_ptr;
  coverpoint F.wr_ptr;
  endgroup
  fifo_cov cov = new;
endmodule
covergroup definition
(like a class)
hierarchical names
covergroup instance
Notes: And note that the “F” in “F.rd_ptr” works here because we instantiated F in this module

## Slide 28: Test #1
Rd_en = wr_en = 1
  Drive new write data every cycle
  Read data every cycle
rd_ptr 0 1 2 3 4 5
wr_ptr 0 1 2 3 4 5
How many of the 8 rd_ptr bins are covered? The 8 wr_ptr bins?
How good of a test is this?
Can we get a more useful coverage measure?
Can we improve our test?
Notes: The FIFO is never full
Is it empty? In fact, given our timing, we continually read an empty FIFO, over and over again 
So the first thing to do is get a better coverage measure that shows how lousy the test is. Then the next task is to improve the test.

## Slide 29: Cross coverage
module tb_top
  fifo #(N_ADDR_BITS, FIFO_WIDTH) F (.*);
  covergroup fifo_cov @(posedge clk) if (!reset);
  rd: coverpoint F.rd_ptr;
  wr: coverpoint F.wr_ptr;
  cross rd, wr;
  endgroup
  fifo_cov cov = new;
endmodule
Full cross-product coverage
Now how many bins?

## Slide 30: Other FIFO improvements?
We’ve checked 8 + 8 + 8*8 bins – that’s thorough 
Is it overkill? Do we really need to cover every one of those, to catch our FIFO bugs?
Bugs are often found at corner cases. What are the corner cases of this FIFO?
  Empty and full. Any others?
  Writing a full FIFO while reading it?

## Slide 31: Cross coverage
module tb_top
  fifo #(N_ADDR_BITS, FIFO_WIDTH) F (.*);
  covergroup fifo_cov @(posedge clk) if (!reset);
  emp: coverpoint F.empty;
  wr: coverpoint F.full;
  endgroup
  fifo_cov cov = new;
endmodule

## Slide 32: Output
A write-only memory is not really useful 
  Simulator tracks coverage
  But how do we actually get the numbers printed?
Detailed beautiful graphical summaries:
  Available in most simulators from the command line
  Simulator-specific (not easily available in edaplayground.com)
Software access is available as per LRM 19.8
  Cov.get_inst_coverage(), cov.get_coverage()
Notes: And I’ve not figured out how to get the beautiful summaries on edaplayground.com

## Slide 33: Mesh coverage
Discussion: what might be good coverage for the mesh?
  predicting FIFO corner cases was easy
  but what are they for the mesh?
Notes: Empty and full on every FIFO in the design? Ring occupancy being high for many cycles? Lots of traffic hitting any given mesh stop?

## Slide 34: Mesh-stop covergroup
Sure, we can declare a covergroup
  but which of the 16 MSs is it covering?
How should we specify which MSs to cover?
  covergroup mesh_cov @(posedge clk);
    vsp: coverpoint vert_sel_pass;
    hsp: coverpoint hori_sel_pass;
    …
  endgroup
  mesh_cov inst = new;
Notes: We probably want to cover all of them… but perhaps not

## Slide 35: Covergroup objects
Object-oriented syntax
  each instance can observe any set of inputs
  e.g., from a different mesh stop
Can we instantiate coverage of our 4x4 MS array?
  covergroup mesh_cov @(negedge clk);
    vsp: coverpoint vert_sel_pass;
    hsp: coverpoint hori_sel_pass;
    …
  endgroup
  mesh_cov inst = new;
(ref input vert_sel_pass, …) @(negedge clk);
inst00 = new (M_NxN.yloop[0].xloop[0].MS.vert_sel_pass);

## Slide 36: Rules to bump into
Hardware elaboration happens before simulation
Module top-level statements typically instantiate hardware, and can execute in any order
Generate loops with for statements do not really generate arrays

## Slide 37: 2D array coverage – take 1
Problems with this?
generate
genvar x, y;
for (y=0; y<N; ++y) : yloop
for (x=0; x<N; ++x) : xloop
mesh_stop #(.MY_Y(y), .MY_X(x)) MS (.vert_ring_in (vert_ring[y][x]), ...);
endgenerate
mesh_NxN.sv
int x,y;
for (y=0; y<N; ++y)
for (x=0; x<N; ++x)
mesh_cov inst00 = new (M_NxN.yloop[y].xloop[x].MS.vert_sel_pass, …);
tb_mesh.sv
Notes: First, we’re creating the entire array and saving it into one variable. I think this will still collect coverage, but it will be hard to read it!
Second, the problem that generated instances are not actually arrays. This will not compile.

## Slide 38: 2D array coverage – take 2
Solution – must instantiate the covergroups from within a generate block
generate
genvar x, y;
for (y=0; y<N; ++y) : yloop
for (x=0; x<N; ++x) : xloop
mesh_stop #(.MY_Y(y), .MY_X(x)) MS (.vert_ring_in (vert_ring[y][x]), ...);
endgenerate
mesh_NxN.sv
generate
genvar x,y;
for (y=0; y<N; ++y)
for (x=0; x<N; ++x)
mesh_cov inst00 = new (M_NxN.yloop[y].xloop[x].MS.vert_sel_pass, …);
tb_mesh.sv
Problems with this?
  The same issue with arrays

## Slide 39: 2D array coverage – take 2b
Solution – actually use an array 
generate
genvar x, y;
for (y=0; y<N; ++y) : yloop
for (x=0; x<N; ++x) : xloop
mesh_stop #(.MY_Y(y), .MY_X(x)) MS (.vert_ring_in (vert_ring[y][x]), ...);
endgenerate
mesh_NxN.sv
mesh_cov cov_arr[MESH_SIZE][MESH_SIZE];
generate
genvar x,y;
for (y=0; y<N; ++y)
for (x=0; x<N; ++x)
cov_arr[y][x] = new (M_NxN.yloop[y].xloop[x].MS.vert_sel_pass, …);
tb_mesh.sv
Problems with this?
  SV top-level statements are not ordered
Notes: So the declaration of cov_arr could be after the assignment to it! This will not compile, either

## Slide 40: 2D array coverage – take 3
Array assignment must go inside of an initial block
Cannot have a generate block inside of an initial block
  generate must happen at elaboration time, but initial block executes at t=0 of simulation
I’ve found one path through this
  See tb_mesh_5b.sv
Notes: So the declaration of cov_arr could be after the assignment to it! This will not compile, either

## Slide 41: Output
Software access is available as per LRM 19.8
  no beautiful graphics, but works the same for all simulators
cov[0][0].get_inst_coverage(good, n_bins)
  returns coverage for that one single MS
cov[0][0].get_coverage(good, n_bins)
  returns coverage for the ensemble of all MSs
  so, lots more bins!
  would cov[0][1] give the same result as [0][0]?
They both also return a percentage number
  100 * n_covered_bins / n_total_bins

## Slide 42: Merging for get_coverage()
cov[0][0].get_coverage(good, n_bins)
What does “the ensemble of all MSs” mean exactly?
  If each one has, e.g., five coverpoints of 1-bit signals
  (2 bins/coverpoint) * (5 coverpoints/inst) * (16 inst) = 160 total bins!
  may not be exactly what you want
Merge_instance mode
  total coverage has same number of bins as any individual instance (10, here)
  each bin counts as covered if any instance covered it
When might each mode be useful?
Notes: Let them answer the question, but don’t comment – mesh lab #4 will help them answer it!

## Slide 43: Single coverpoints
What if we want to check coverage on vert_sel_pass and hori_sel_pass individually?
  cov[0][0].vsp.get_coverage(good, n_bins)
  requires option.per_instance=1
  covergroup mesh_cov @(negedge clk);
    vsp: coverpoint vert_sel_pass;
    hsp: coverpoint hori_sel_pass;
    …
  endgroup
option.per_instance=1;