## Slide 1: Verification
Spring 2022
Tufts University
Instructors: Joel Grodstein, Scott Taylor
SystemVerilog

## Slide 2: Outline of this lecture
Quick overview
Basics: datatypes, variables, expressions, etc
Simulation and races
Always & initial blocks
Static vs. automatic

## Slide 3: SystemVerilog education
Books free at Tisch
  SystemVerilog for Verification: A Guide to Learning the Testbench Language Features by Chris Spear
  Verilog and SystemVerilog gotchas : 101 common coding errors and how to avoid them by Stuart Sutherland
  Official Language Reference Manual: IEEE Std 1800-2017. 1300 pages, but well organized 
Sunburst design: http://www.sunburst-design.com/papers/
  lots of good stuff, targeted at professionals
verificationacademy.com
stack exchange, etc.
Numerous textbooks available for purchase

## Slide 4: Module
A module is the basic unit of organization in SV
  Like a VHDL entity and architecture combined
  Typically, each module is one file

## Slide 5
module mesh_stop #(parameter MY_Y=0, MY_X=0)
(input Ring_slot data_from_venv, … // incoming packets
input logic reset, clk,
output Ring_slot data_to_venv);
  logic DrvF_rd_en, …;
  always_comb begin
    unique if (vert_sel_pass) vert_mux_out = vert_ring_in;
    else vert_mux_out=EMPTY_RING_SLOT;
  end
  always_ff @(posedge clk) begin
  if (reset)
  vert_ring_out <= EMPTY_RING_SLOT;
  end
  fifo #(.DATA_TYPE(Ring_slot)) VRxF(.reset(reset), .clk(clk),…);
endmodule
this is a module!
compile-time params
C++-style comments
input & output wires, busses
internal wires
combinational logic (a mux)
instantiate child module(s)
a flop (bad code)
“…” is not official syntax!
data types
Notes: Hopefully this level of code is pretty self-explanatory.,
Note that, in principle, the mesh lecture isn’t until #8 (this is lecture #3).
The “bad code” for the flop is that the output is only driven during reset

## Slide 6: Outline of this lecture
Quick overview
Basics: datatypes, variables, expressions, etc
Simulation and races
Always & initial blocks
Static vs. automatic

## Slide 7: Datatypes
Spear ch. 2; LRM ch. 6
SystemVerilog is for both HW and verification!
Basic types
  Bit (2-state signal), logic (4-state signal); see next page
  Int, short int, etc. are wider versions of bit
There’s more (reg vs. wire vs. var), but you can almost always ignore that
  SystemVerilog infers the correct one
Class types (that’s what ring_slot was)
Strings (i.e., types for programming, not just HW)
Notes: Why not have wider versions of “logic”? Because HW wires are 1 bit wide; wider is via arrays.

## Slide 8: 4-state quirks
2-state (bit): can be 0 or 1
4-state (logic): 0, 1, X, Z
What does this really mean?
Z = high impedance
  A wire is undriven
  We won’t use Z much
X = unknown/undefined
  Wire is at an intermediate voltage value
  Wire is at 0 or 1, but we don’t know which
  Typically happens around reset, multiple drivers, other HW errors
  A Big Deal for verification
verification
HW

## Slide 9: 4-state quirks
2-state: can be 0 or 1
4-state: 0, 1, X, Z
But if a and b are 4-state, what does == mean?
  Compare normally, except: any bit of either operand X means the result is X
  Note that if (1'bX) treats 1'bX as false
Examples
  2'b00 == 2'b01 →
  2'b0X == 2’b01 →
  2'b0X == 2’b0X →
!= also yields 1'bX if there’s an X or Z anywhere
1’b0
1’bX
1’bX

## Slide 10: Initialization
From LRM Table 6.7:
  2-state values default to 0
  4-state values default to X
Arrays are no different
You can override either one with the syntax
  logic foo = 1’b1
  many other syntaxes available for your convenience

## Slide 11: More fun with ==
New equality operators:
=== compares bit by bit with X===X and Z===Z
  result can only be 1'b0 or 1'b1
  2'b0X === 2'b0X → 1'b1
  2'b0X === 2'b01 → 1'b0
  !=== is obvious
==? treats X,Z as wildcards in the right operand:
  2'b01 ==? 2'b0X → 1'b1
  2'b0X ==? 2'b01 → 1'b0
The spec is not clear what !==? does 

## Slide 12: Constants
5'b10001 # 5-bit binary
16'hab1f # 16-bit hex
byte a # 8 bits
a = 1'b1 # A ‘1’, sign extended to fill 8 bits

## Slide 13: Strings
Reminder – mostly for programming, not for HW
string my_str; // declare it
my_str = "abc" // initial assignment
my_str = {my_str, "def"} // concatenate to "abcdef"
len (my_str) // 6

## Slide 14: Arrays
Spear ch. 2; LRM ch. 7
Arrays are how we turn logic into busses, regfiles, etc.
An array can be packed or unpacked
  Packed array of bit or logic will be contiguous in memory; can do arithmetic on multiple-bit field
  Packed only applies to bit or logic; cannot pack anything else
Examples
  logic [7:0] a; // 8-bit packed. Can say a[3:1] = 3'b100
  logic a [7:0]; // 8 single-bit unpacked items
  logic [7:0] a [13:0]; // 14 items, each 8-bit packed
  // e.g., a register file
Both types of subscripts can be multi-dimensional
Can have dynamic arrays as well

## Slide 15: Quirks of arrays
Array subscripts
  foo[7:0] ≠ foo[0:7] (can bit-swap an array param!)
  foo[8] is a declaration shortcut for foo[0:7]
  LRM
Array access
  accessing out of bounds is not illegal
  logic foo[7:0]; foo[100000] typically returns zero!
  LRM 7.4.6
but only legal on unpacked subscripts!

## Slide 16: Statements
“Mostly” like C++
  For loops, while loops, if, break, continue, comment characters, typedef, enum, …
  But begin end rather than { }
  See Spear ch. 3
Why have statements?
  Couldn’t write verification code without them
  They can make it easier to write HW too
if (sel)
  out=a;
else
  out=b;
for (int i=1; i<n_flops; ++i)
  flops[i] <= flops[i-1];
Notes: The left example is a mux.
The right example is a shift register.

## Slide 17: Objects
Similar to C++
See Spear ch. 5, ch. 8; LRM ch. 8
We’ll use them when we get to the mesh

## Slide 18: Instantiating modules
Numerous flavors are available (LRM ch. 23)
  shortcuts where parent & child names match
  parameter passing
  arrayed instances
module full_adder (input logic a, input logic b, input logic cin,
output logic cout)
half_adder ha1 (.in1(a), .in2(b), .sum(a_xor_b), .car(ab));
xor gate1 (cout, a_xor_b, c);
and gate2 (a_xor_b_and_c, a_xor_b, c);
or gate3 (cout, a_xor_b_and_c, ab);
endmodule : full_adder

## Slide 19: Outline of this lecture
Quick overview
Basics: datatypes, variables, expressions, etc
Simulation and races
Always & initial blocks
Static vs. automatic

## Slide 20: Race model
Consider the following circuit
in
Q2
D Q
D Q
Q1
clk
in
clk
Q1
Q2

## Slide 21: Race model
Consider the following circuit
in
Q2
D Q
D Q
Q1
clk
cclk
Q2
cclk
Q1
in
clk

## Slide 22: How to deal with races?
VHDL and SystemVerilog each specify how to simulate
Each have a different solution
Won’t learn the details
  Will learn how to get what you want 
Notes: See https://www.thecodingforums.com/threads/vhdl-processes-race-conditions-verilog.23520 for VHDL

## Slide 23: Backup
SystemVerilog:
  Everything can be simulated
  A subset can be synthesized to hardware
  Operation of the simulator is mostly well defined
See:
  SystemVerilog Event Regions, Race Avoidance & Guidelines, SNUG 2006
  LRM ch. 4
Simulation time starts at t=0, moves forward
  Each timepoint divided into regions
  Each region can have lots of simulation (but all at the same timepoint)
  Main regions are Active, NonBlocking Assignment

## Slide 24: Outline of this lecture
Quick overview
Basics: datatypes, variables, expressions, etc
Simulation and races
Always & initial blocks
Static vs. automatic

## Slide 25: always_comb
Put all combinational logic in always_comb blocks
  Don’t put flops here
Use “=” for assignment
  blocking assignment
When any external input (a or e) changes, the entire block runs
  All statements executed in order
  d = a+b+c will likely have an unexpected result (c isn’t assigned yet)!
always_comb begin
  b = e + 5;
  d = a + b + c;
  c = e + 2;
end
Notes: Yes, you may wind up with flop-like behavior on d. But you may not, if this block gets executed twice in the same (or nearby) time slots.

## Slide 26: always_comb
Put all combinational logic in always_comb blocks
  Don’t put flops here
Use “=” for assignment
  blocking assignment
What do you think about this “if” statement?
  bad practice!
always_comb begin
  b = e + 5;
  if (clk)
    d = a + b + c;
  c = e + 2;
end

## Slide 27: always_ff
Put flops here
When clk changes, the entire block runs once
Note <= rather than =
  Non-blocking assignment
  Idea is to avoid races
  Inputs are all sampled “now,” and then assigned “later”
always_ff @(posedge clk) begin
  b <= e + 5;
  d <= c + a;
end
D Q
D Q
clk
e+5
c+a
b
d

## Slide 28
Race-free – does what you want
Order of the blocks is irrelevant
Execution order
  clk changes
  cclk changes
  in is sampled
  Q1 is sampled
  Q1 updated
  Q2 updated
in
Q2
D Q
D Q
Q1
clk
cclk
always_ff @(posedge clk) begin
  Q1 <= in;
end
always_ff @(posedge cclk) begin
  Q2 <= Q1;
end
always_comb begin
  cclk = clk & foo
end
Notes: You don’t have to know these details – if you follow the always_comb & always_ff rules, it will all just work
The bracketed assignments may execute in either order

## Slide 29: always_ff
Class exercise: what does this do?
What if we swapped the order of the two statements?
Compare this to the equivalent C++ code
always_ff @(posedge clk)
  b <= a;
  a <= b;
end
D Q
D Q
clk
a
b
Notes: because inputs are sampled before the clock & outputs assigned later

## Slide 30: always_ff
How about this one?
This one makes no sense; cannot assign b two different values
  Compiles fine, but it’s a race
  Never know which assignment will happen first
  Not sure how to even draw this in hardware!
always_ff @(posedge clk)
  b <= a;
  a <= b;
  b <= c;
end

## Slide 31: always block details
Each always_comb or _ff block is a separate thread
  Threads execute in arbitrary order
When any always* block executes, it’s done
  Until the next time an input changes
  And the entire thread gets scheduled again
always_ff @(posedge clk) begin
  Q1 <= in;
end
always_ff @(posedge cclk) begin
  Q2 <= Q1;
end
always_comb begin
  cclk = clk & foo
end
Reference: SystemVerilog Logic-Specific Processes for Synthesis‐ Benefits and Proper Usage, SNUG 2016

## Slide 32: Initial blocks
always_comb and always_ff blocks execute every time an input changes
initial block happens just once, at the beginning of the sim
Purpose?
  For verification only (not for hardware)
  Open files
  Launch packets from verification environment → mesh
  Kick off clock(s)
  And on and on…

## Slide 33: Outline of this lecture
Quick overview
Basics: datatypes, variables, expressions, etc
Simulation and races
Always & initial blocks
Static vs. automatic

## Slide 34: Static vs. automatic
SV has static and automatic variables (like C)
  Automatic: old value is lost when they go out of scope
  Static: old value is retained when they go out of scope
void f() {
static int i=5;
++i;
cout << i << endl;
}
f(); f();
void f() {
int i=5;
++i;
cout << i << endl;
}
f(); f();
Class exercise: what do these two examples print (this is C code)?
Notes: This is C code -- SV code will be on the next slide.
The left example prints 6 6; the right example prints 6 7.

## Slide 35: Static vs. automatic
In SV, most things default to static
  Came from Verilog, which is a hardware language
  Hardware doesn’t have a stack
module my_mod;
function void f();
int i=5;
++i;
$display (“%d”, i);
endfunction : f
f(); f();
endmodule : mymod
6
7
automatic function void f();
automatic int i=5;
automatic module my_Mod;

## Slide 36: Static vs. automatic
Guidelines:
  declare all modules automatic
  and module-level variables
  and functions, just to be safe!
Compilers often warn you if you try to initialize a static variable
See Spear ch. 3; LRM 10.5
module my_mod;
function void f();
int i=5;
++i;
$display (“%d”, i);
endfunction : f
f(); f();
endmodule : mymod

## Slide 37: BACKUP
add these in next year
Don’t use if statements in an always_comb block except to implement a mux; they’ll often turn into an unintended latch