## Slide 1: Verification
Spring 2022
Tufts University
Instructors: Joel Grodstein, Scott Taylor
Building the mesh

## Slide 2: Building a mesh
Main design for this course: a mesh
  N x N grid of mesh stops (MS)
  Interconnected by a fabric
  2D mesh; ring of rings
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 3: Building a mesh
One ring
  Allows mesh stops to send packets to each other
Anything physically silly about this ring?
  More efficient if it made stops on the way back
  But more complex also! We’ll do the easy version 
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Notes: The very long right-to-left wire on top passes right by the other stops. So why not drop data off or pick it up as you’re passing by?

## Slide 4: Example
Route from 01 → 13
Any other way to skin the cat?
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 5: Example
Route from 01 → 13
Any other way to skin the cat?
  Vertical-first or horizontal-first
  Or even zig-zag 
  All are fine; we’ll choose vertical-first
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 6: MS as a black box
Each MS interfaces to the mesh via vertical & horizontal rings
Anything missing?
  Each MS can receive a packet from the environment at the packet’s source MS
  And deliver at the packet’s destination MS
vert in
vert out
hori in hori out

## Slide 7
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
taking_data
data_avail_for_venv
can_accept_data_from_venv

## Slide 8: Example
Route from 01 → 13
Verif. environment giving packet to MS01, onto vertical ring
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 9
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
taking_data
data_avail_for_venv
Verif. environment giving packet to MS01, onto vertical ring
Drive empty → horizontal ring
can_accept_data_from_venv

## Slide 10: Example
Route from 01 → 13
Ring turn at MS11
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 11
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
taking_data
data_avail_for_venv
Ring turn at MS01; drive empty packet → vertical ring
can_accept_data_from_venv

## Slide 12: Example
Route from 01 → 13
Pass through MS12
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 13
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
taking_data
data_avail_for_venv
Pass through MS02
Drive empty → vertical ring
can_accept_data_from_venv

## Slide 14: Example
Route from 01 → 13
MS13 receives packet & gives to verif. env
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 15
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
taking_data
data_avail_for_venv
Receive packet, give to verif. env
Drive empty → horizontal ring & vertical ring
can_accept_data_from_venv

## Slide 16: Other paths
Route from 12 → 13
No need to use a vertical ring
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 17
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
taking_data
data_avail_for_venv
Packet destination Y = source Y
No need to use a vertical ring
can_accept_data_from_venv

## Slide 18: Other paths
Route from 12 → 22
No need to use a horizontal ring
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 19
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
taking_data
data_avail_for_venv
Packet destination X = source X
Vertical ring straight to VEnv
can_accept_data_from_venv

## Slide 20: Done with MS v1
Basic operation is reasonably straightforwards
Next addition to make MS v2 – timing
  Our mesh has no flops at all!
  We need pipelining – but where?

## Slide 21
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
hori_sel_*
data_to_venv
empty
empty
empty
data_from_venv
taking_data
data_avail_for_venv
can_accept_data_from_venv

## Slide 22: Done with MS v2
Basic operation is reasonably straightforwards
And the timing is reasonable
  Packets move one hop every cycle
  I.e., move through one MS every cycle
Next problem is bigger
  Can our mesh handle >1 packet at a time?

## Slide 23: Two packets at once – easy
Route from 01 → 13
Route from 23 → 30
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 24: Example
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Route from 01 → 13
Route from 23 → 30

## Slide 25: Example
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Route from 01 → 13
Route from 23 → 30

## Slide 26: Example
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Route from 01 → 13
Route from 23 → 30

## Slide 27: Example
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Route from 01 → 13
Route from 23 → 30
Piece of cake 
But…

## Slide 28: Example
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Route from 23 → 30
Route from 32 → 31
  Note no vertical route needed for this
  A special case, but that’s not our problem

## Slide 29: Example
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
Route from 23 → 30
Route from 32 → 31
Both packets want to go through MS33
Can they?

## Slide 30
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
taking_data
data_avail_for_venv
M23 → M30 in red
M32 → M31 in blue
They cannot both use the same wires 
can_accept_data_from_venv
Notes: Note that the wires *after the flop* represent a conflict in the next cycle, not the current one

## Slide 31: MS v3
Add FIFOs so that packets can wait for busy resources to become free

## Slide 32
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
M23 → M30 in red
M32 → M31 in blue
can_accept_data_from_venv

## Slide 33
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
data_to_venv
empty
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
Data_avail_for_Venv when HRxF is !empty
Venv handshakes when it wants to
can_accept_data_from_venv

## Slide 34: That’s our mesh stop
That’s the basic operation
More subtleties can be found by looking at the control logic

## Slide 35: Ring signal names
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33
VR00
VR10
VR20
VR30
HR00
HR01
HR02
HR30
Summary: mesh stop #y,x drives both HRyx and VRyx.

## Slide 36: MS signal names
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
hori_sel_*
vert_sel_*
toVenv_sel_*
data_to_venv
VRxF_out
HRxF_out
empty
DrvF_out
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
can_accept_data_from_venv

## Slide 37: Vertical mux selects
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
hori_sel_*
vert_sel_*
toVenv_sel_*
data_to_venv
VRxF_out
HRxF_out
empty
DrvF_out
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
can_accept_data_from_venv
vert_sel_pass
vert_sel_me
vert_sel_empty

## Slide 38: Horizontal mux selects
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
hori_sel_*
vert_sel_*
toVenv_sel_*
data_to_venv
VRxF_out
HRxF_out
empty
DrvF_out
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
can_accept_data_from_venv
hori_sel_pass
hori_sel_turn
hori_sel_me
hori_sel_empty

## Slide 39: toVenv mux selects
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
hori_sel_*
vert_sel_*
toVenv_sel_*
data_to_venv
VRxF_out
HRxF_out
empty
DrvF_out
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
can_accept_data_from_venv
dtvenv_sel_HRxF
dtvenv_sel_VRxF
dtvenv_sel_empty

## Slide 40: Handshakes to/from vEnv
vert_ring_in
vert_ring_out
hori_ring_out
hori_ring_in
hori_sel_*
vert_sel_*
toVenv_sel_*
data_to_venv
VRxF_out
HRxF_out
empty
DrvF_out
empty
empty
data_from_venv
Drv FIFO
VRx FIFO
HRxF FIFO
taking_data
data_avail_for_venv
can_accept_data_from_venv

## Slide 41: Mux prioritization
vert_sel_pass: highest priority; probably the oldest. And where else could it easily go?
vert_sel_me: next highest
vert_sel_empty: if there’s nothing else to drive
hori_sel_pass: ditto
hori_sel_turn: probably still older than me
hori_sel_me: ditto
hori_sel_empty: ditto
Notes: In principle, we could make sel_pass a lower priority without breaking the mesh. Incoming “pass” packets would get stuffed into the appropriate receiver FIFO and then pushed back out onto the ring when a slot opens. But that’s a bit harder than what we did.